KIK Panthea Court _ Apartment 101

Plot:		636, section 06, s/d 54/420503, Mesa Yeitonia, Lemesos

Apartment:	ΚΙΚ Panthea Court 101

Buyer Name:

--------------------------------------------------------------------------------------------------------------------------------------------------

APARTMENT GENERAL SPECIFICATION

1. STRUCTURAL FRAME

Steel frame on Reinforced Concrete Foundation, according to specification and current antisismic code and regulations . The external frame is insulated with

50 MM extruded polystyrene for beams and columns and 25 MM ordinary plaster . Also 50 MM Styrofoam

for roof slab and waterproofing insulation.

2. WALLS

Exterior walls made of Gypsum Board, insulated my 80mm rockwool within the wall structure, as well as an added 50mm certified ETICS system.

3. WALL FINISHES

All Internal surfaces are finished in three coats spatula Uniflott®, one coat Emulsion  Primer NEOPAL and three

coats of SUPER NEOPAL mate paint.

External surfaces are finished in specified ETICS system finish.

4. FLOORING

Living room – Dining room Ceramic Tiles or marble €20.00 per m²

Bedrooms Laminate Flooring 10mm (AC4/32) €15.00 per m²

Kitchen Ceramic Tiles or marble €20.00 per m²

Corridors Ceramic Tiles or marble €20.00 per m²

Stairs Marble €25.00 per running meter

Bathrooms Ceramic Tiles €20.00 per m²

Verandas Ceramic Tiles €15.00 per m²

5. DOORS AND WINDOWS

a) The Entrance Door is made of solid wood construction.

b) All external fixed and hinged doors and windows are double-glazed and are made of aluminium frames

by Muskita Industries.

c) All external sliding doors and windows are double-glazed and are made of aluminium

frames.

d) Glazing for all external doors and windows is 6mm iPlus S + 5mm clear glass.

e) All aluminium frames and louvers will be anodized in silver anodizing colour from Mouskita anodizing pallete.

f) All internal doors are made of M.D.F finished with a paint finish.

g) There will be a provision for electrical rolling shutters for external windows (external type).

6. WARDROBES & CABINETS

Built-in opening wardrobes are made with a melamine finish.

Kitchen Cabinets and cupboards are made internal with a melanine, and externally finished with melanine

Incorporating bench tops made of granite.

7. WALL TILES

Kitchen Ceramic Tiles €25.00 per m²

Bathrooms Ceramic Tiles €25.00 per m²

8. SANITARY WARE/FITTINGS

Sanitary ware is white and of deluxe quality, and the fittings are chrome plated.

9. BALUSTRADES/FENCING/BOUNDARYWALLS

Veranda balustrades are constructed of Aluminium and glass.

10. ELECTRICAL INSTALLATION

The project Electrical installation is divided in to two main parts as below:

Part A Common Areas

Part B Apartments Areas

Common Area Services

 Distribution boards and protection devices.

 Lighting circuits for the basement, entrance lobby, parking area, front entrance, staircase, apartments lobbies and roof plan. The circuits will be controlled either via staircase timers, motion sensors, time switches and light switches.

 Emergency lighting for the staircase, apartment lobbies and entrance lobby.

 Sockets circuits for the entrance lobby and parking area.

 Small power circuits for the lift control panel, electric barriers, electric water heater and  air conditioning internal units.

 Wi-Fi points

 IP Colour Video Door Phone with access control having external units and six internal units for apartments.

 Complete Telephone system, conduits and wirings for all apartments for the services provider connection.

Apartments

 Distribution Boards and protection devices.

 Lighting circuits.

 Sockets circuits.

 Small power circuits for the cooker, oven, dish washer, w/machine, refrigerator and air conditioning units.

 Shutter circuits for the bedroom windows.

 Conduit provision for wireless security system.

 Structured cabling complete with wiring and patch panels providing ethernet connection points for all TV point (for smart displays) and additional points for the kitchen, master bedroom and sitting room.

 IP Colour Video Door Phone with access control.

 TV system for local channels reception and conduit provision for satellite dish.

11. PLUMBING & DRAINAGE

a) Cold-water installation includes a 1.0m3 P.V.C. storage tank and water pressurisation unit on the roof.

The main domestic cold and hot water pipes from the plantroom up to the manifolds are made of multilayer PPR. The domestic cold and hot water pipes from the manifolds up the sanitary fittings will Pex pipe-in-pipe.

b) There is a domestic hot water recirculation system which includes pump, pipes and push-button outside

each bathroom. When this system is activated by the push-buttons, hot water is circulated in the pipes

and is brought nearer to the tab, to avoid water waste.

c) Solar system is installed on the roof and is comprised of a hot water cylinder 100 lts and 3.6m² collectors for3bedroom apts. For the2-bedroom apts the cylinders will be 160lts and the collectors 3.6 m²

d) The hot water cylinders are equipped with a backup electric heater 3kw.

e) All drainage pipes are U. P.V.C. The drainage system is connected to the city sewer.

12. AIR CONDITIONING & HEATING

Provision for 2 Air Conditioning Split Type Units that are placed on Wall surfaces.

CHANGES TO THE SPECIFICATIONS & DRAWINGS

The Purchaser may request changes to the specification or drawings, the cost of which is negotiable, however the Vendors reserve the right to refuse any changes, which are considered as unsafe and outside good building practice or spoiling the architectural design and/or the character of the project.